Setup Files:

-EGOUT-Setup ------------------setup EGOUT

-Egout.exe for acad xxxx--------EGOUT Run file for ACADxxxx

-Egout DWG sample---------------Work  step by step

Run EGOUT

1-run setup exe in folder EGOUT-Package

press ok for all questions

2-copy EGOUT.exe from EGOUTXXXX to HARD disk( or egout.exe from egout.zip for

acad2XXX to EGOUT-acad2XXX  folder )

3-open acad2XXX

4-run EGOUT.exe

5- press Start for connect to acad

6- if ACAD version not match with EGOUT ( error Type mismatch displayed)

7-in ACAD window:

7-1-set sewer layer current (layers automatically makes with EGOUT)

7-2-draw line end to end with LINE command (sewer line drawn in sewer layer-see         example 1)

7-3-Insert Endblock to endpoint of sewer network( outfall point)

NOTE: (End block is a block refrence makes with EGOUT insert it with   Insert command in Acad commend line

Edit net work-press EDIT button

Set Lateral by change color on sewer line in upstream and Then Setlatral in EGOUT window

In EGOUT :

Color 1(red) is Main sewer

2(yellow) is sub main

3(green) is sub main

4,5,6(cyan,blue and magenta) is lateral

For Lateral Name Press Latname

For change  Latname(*1) to another name( A,B,…) Edit attrib of latblock( insert in to downstream line with EGOUT automatically)

You can insert latblock in other main(see above picture)

For manhole numbring press Mhname bottun in EGOUT window.

Elevation SET

Change layer elevation code( Text only) to elevation layer

Press Elv-set

With interpolation elv text insert By EGOUT

You can change search radius in  Value box in EGOUT window and Elv-set Egain for find other code

You can edit theas code with DDEDIT command in ACAD

Press GELV bottun in EGOUT for move text code to Z of sewer line( error 5 for Gelv=0)

For Region draw close region with line in area-density layer

Density Input (D1,D2 in density layer)

Population Input (P1,P2 in density layer)

Save ur Design Dwg

Get data With Getdata bottun in EGOUT window

For input Project info Press Project in EGOUT window

Taitle

Criteria

Populatin  option

Infiltration Measure

INFLOW measure

STORM data

Q=2.78 C.I.A.B

Diameter Window

Sewer Window

SOLVE-press solve bottun

View: you can view Sewer network profile in VIEW window

You can select line with Right click on profile and edit slope and cover of each line

Press SDF for Slope defind by user( sdf fix slope with designer)

Search